Method Statement – Pumping/Tankering 1. Intent and Introduction Method Statement for Pumping/Tankering. This procedure is widely used in A1 Wet Waste Ltd undertakings. Although the location will change due to the reactive nature of the Companies processes. Hazards related to any location may vary but the operation and use of any pumping appliance should remain constant.

2. Locations

3. Description of Works To attend site and remove liquid waste and light solids as directed on site. Pumping is used in the Drainage Industry for the removal of unwanted substances generally excess water. On arrival to site all A1 Wet Waste Ltd employees must report to the pre arranged meeting point. Site will be under the control of the appointed site supervisor whose instructions will be obeyed at all times. An on site risk assessment will be carried out by the site supervisor or charge hand. Any changes from the site risk assessment will be noted and appropriate measures taken to control the risks identified. Work will not commence until procedure 3 is completed. If risks cannot be controlled works must be abandoned until appropriate control measures in place and works safe to continue. All A1 Wet Waste Ltd employees will undergo a site induction. All site rules will be understood and adhered to. A1 Wet Waste Ltd employees are to be reminded on dangers of working on site. See generic risk assessment “working on site”. Safe access will be made to the point of works. All site safety rules will be followed throughout the operations including access and egress to point of works and site speed limits. Safe positioning of all company vehicles around work site ensuring our Safety at Street Works and Road Works code of practice is adhered to. The working area must be suitably protected via the use of barriers and cones. See generic risk assessment on “street works / road works”. When all safety barriers are in place around required manholes then manhole covers can be raised. See manual handling assessment on lifting manholes. Once the chamber has been adequately ventilated an atmosphere test using a gas monitor must be obtained. The outcome of this test will determine whether works will be permitted. If the test is a pass operations are permitted following the instructions below. If the test is a fail no works will commence. All chamber access covers will be replaced and all A1 Wet Waste Ltd employees will leave the site ensuring it is left in a safe condition. Again following all site safety rules and regulations. If the atmosphere test has passed. Set up an equipment dump with all the pumping equipment needed. Inspect all fixtures and fittings of hose equipment. Connect all the appropriate couplings. Ensuring all couplings are of correct standard and fit. Connect the required lengths of suction hose. The person operating the pumping appliance must be competent and wearing the correct PPE. See generic risk assessment Pumping Locate the required position to place the suction hose. When all the suction hose is correctly connected and all operatives are informed pumping operations may commence. Continue pumping until removal or required level has been achieved. The suction hose may have to be moved during operations to ensure a constant lift. Remember the hose weight will have increased due to being full of contaminates. It may require you to switch off the PTO to lose the lift thus empting the suction hose making it easier to move. When pumping operations have stopped remember manual handling techniques when lifting suction hose. Replace manhole cover immediately. Remembering the correct manual handling procedure. If pumping appliance is full and you must empty your tank before returning to continue pumping. On your return start again from method statement point. Ensure all equipment is checked, cleaned and stowed away. When safe to do so ensure covers are replaced, barriers removed, the work area cleaned and disinfected and the site is left in a safe condition. Leave the site ensuring it is left in a safe condition. Again following all site safety rules and regulations. Report any defects, faults or operational problems immediately to your supervisor.

4. Plant and Equipment A1 Wet Waste pumping appliance. Suction hose. Eye protection ( safety goggle). Foot protection. Ear protection. Head protection. Body protection. Manhole keys. Cones and barriers. Lighting. Manhole cover lifting aids.

5. Related Documentation and Assessments Manual handling assessment manhole covers. All generic risk assessments. Safety at Street Works and Road Works Code of Practice. Health and Safety and Environmental Policy.

6. Location and Protection of any Services/Facilities affected by Works Customer to advise.

7. Foreseeable Adverse Effects and their Control Working near to water. See risk assessment on Working in water and working near to water. A1 Wet Waste Ltd supervisors take over all responsibility of operations and retain the right to cancel or halt any operations as they deem necessary. Works may need to be re scheduled if initial assessment of site deems this method statement as unviable. Please see attached site specific risk assessment.

8. Safety Precautions First Aid Kit PPE. Eye protection (safety goggle). Foot protection (safety boots / wellingtons). Ear protection. Head protection (hard hat). Body protection (water proofs).

9. Monitoring Systems Near miss reporting. Accident reporting. Site inspections.

10. Further Information/Observations. A1 Wet Waste Ltd supervisor’s or charge hand take over all responsibility of operations and retain the right to cancel or halt any operations as they deem necessary. Works may need to be re scheduled if initial assessment of site deems this method statement as unviable. Please see attached site specific risk assessment.

11. Emergencies First aid equipment is provided on each vehicle Emergency services Dial: 999 Call 999 in the event of an emergency and state the incident location as site address or other Follow the instructions of the 999 call handler/emergency medical dispatcher until help arrives. Care must be taken to ensure that access for emergency vehicles is maintained throughout the site operations. Nearest Hospital:

| Method statement prepared by: | Steven Cummings |
| --- | --- |
| Signed |  | Date |  |

Engineers Signature:

When on site to confirm you have read and understood the content of this method statement.

……………………………………………………………………………

……………………………………………………………………………

……………………………………………………………………………

……………………………………………………………………………

……………………………………………………………………………

……………………………………………………………………………

……………………………………………………………………………