Method Statement - Confined Space Manual Entry Intent and Introduction This method statement is for the proposed work involving Confined Space Manual Entry. This is purely a method Statement for works and is not a risk assessment, please see attached Risk Assessment for related hazards and controls. Please note it is the responsibility of the proprietor / person responsible for works to ensure that there are no other hazards introduced from their own acts or omissions, or from others instructed by them. It is the responsibility of the supervisor to ensure that this method statement is adhered to and works must be halted if any hazards or risks occur that have not been suitably controlled.

2. Location of Work: ( Insert full address of site )

3. Description of Work To carry out Confined Space Manual Entry. All works are weather reliant. Forecast reports shall be obtained and no works shall commence if rain is expected or heavy rainfall has not suitably drained away. On arrival to site all A1 Wet Waste Ltd employees must report to the pre arranged meeting point. Site will be under the control of the appointed site supervisor whose instructions will be obeyed at all times. An on site risk assessment will be carried out by the site supervisor. Any changes from the site risk assessment will be noted and appropriate measures taken to control the risks identified. Work will not commence until procedure 3 is completed. If risks cannot be controlled works must be abandoned until appropriate control measures in place and works safe to continue. All A1 Wet Waste Ltd employees will undergo a site induction. All site rules will be understood and adhered to. A1 Wet Waste Ltd employees are to be reminded on dangers of working on site. See generic risk assessment “working on site”. Safe access will be made to the point of works. All site safety rules will be followed throughout the operations including access and egress to point of works and site speed limits. Safe positioning of all company vehicles around work site ensuring our Safety at Street Works and Road Works code of practice is adhered to. The working area must be suitably protected via the use of barriers and cones. See generic risk assessment on “street works / road works”. When all safety barriers are in place around required manholes then manhole covers can be raised. See manual handling assessment on lifting manholes. Once the chamber has been adequately ventilated an atmosphere test using a gas monitor must be obtained. The outcome of this test will determine whether works will be permitted. The gas monitor will be lowered into the chamber and the first reading taken after 5 minutes this will be recorded on an A1 Wet Waste Ltd Space Entry Permit the gas monitor will remain in the chamber while works are undertaken and constantly monitored and recorded. If the atmosphere test has passed. When the Confined Space Entry Permit has been issued the confined space entry can commence Ensure all water entry points to chamber have been isolated therefore removing the risk of water entering the chamber throughout operations. Set up the personal winching equipment and an equipment dump near to operations. The equipment dump should include. Gas detectors. Personnel winch. 1 x Lifelines 10m long. Hand line for lowering equipment. Tripod x1 First aid kit Portable lighting. Escape breathing apparatus. 1x Cf10 escape set . Before entry check for unusual smells and carry out a visual check of the stability of the structure, ladders, step irons etc. Set up winching system and ensure all personnel entering the confined space don and carryout pre use checks on their safety harness, protective equipment and Escape breathing apparatus. If a gas or structural hazard is identified abandon entry as explained in section 9. The competent person in charge of the operation completes the Permit to Work and leaves it with the designated top man. Attach lifelines to all persons entering the confined space and means of communications. With the gas detector in position in the confined space the top man will attach the winch cable to the safety harness of the man entering the confined space. The top man will control the winch as the man climbs down in to the confined space. See generic risk assessment on confined spaces. A gas detector will be worn by every person within the confined space.fixed to their harness at an acceptable level to allow the gas monitor to work in the correct manner When on this site National Classification 2 class A winch entry one entrant one top man required (see classification A1 Wet Waste code of conduct ) There will be 1 person out side of the confined space acting as top man on the winch and in constant contact with the entrant they will be identified on the A1 wet waste Confined Space Entry Permit All equipment used in confined space will be lowered or raised, not carried down. The atmosphere will be constantly tested throughout operations. If test fails escape breathing apparatus will be used to assist in escape. All equipment must be left in situ. The gas detector at the entry point will be constantly monitored by the top man. The working crew must be removed from the confined space after 45minutes work, for a 15 minute break before re entry to the confined space. Pumping operations if required on this site (Interceptors) will be undertaken by tanker crews with no entries to be made All contaminate removed must be disposed of correctly. When the operations have finished. All equipment and personnel must exit the confined space. The CP2 in charge shall account for all personnel and record this. On completion of the works. Ensure all equipment is checked, cleaned and stowed away. When safe to do so ensure covers are replaced, barriers removed, the work area cleaned and disinfected and the site is left in a safe condition Report any defects, faults or operational problems immediately to your supervisor.

4. Plant and Equipment AP2 MAN ENTRY EQUIPMENT 2 x Gas detectors. 1 x Personnel winch. 1 x Lifelines. Hand line for lowering equipment. First aid kit Torch and vehicle lighting 2 x Escape set CF10 1x Tripod Any Specific PPE deemed required by A1 Wet Waste Ltd

5. Related Documentation and Assessments Site specific Risk Assessment. All generic Risk Assessments. Code of Practice for Work in Confined Spaces Confined Space Entry Permit Safety at Street Works and Road Works Code of Practice. Health and Safety and Environmental Policy

6. Location and Protection of any Services/Facilities Affected by Works All water flowing pipes must be isolated to prevent water entering chamber whilst works are being undertaken. Customer to advise.

7. Foreseeable Adverse Effects and their Control Weather conditions: control weather forecast must be obtained before any works commences. Works must only be carried out on a clear dry day. There should be no chemicals or substances liable to cause harm. All personnel must be trained and competent, wearing gas detectors, lifelines, safety harness and escape breathing apparatus.

8. Safety Precautions Escape breathing apparatus. Gas detectors. Personnel winch. Lifelines. First aid kit. The use of a safety man at the access and egress point to monitor works and improve communication with top man. Constant atmosphere testing throughout operations.

Monitoring Systems Designated Supervisor or Team Leader (Insert Name) to over see complete operations. Top Man to operate winch monitor entry have phone to contact emergency services. Safety man in position to monitor working crew and assist in communications. Gas monitoring to constantly monitor atmosphere.

Further Information/Observations A1 Wet Waste Ltd supervisors take over all responsibility of operations and retain the right to cancel or halt any operations if they deem the works or site unsafe they will contact the contractors site manager and inform him/her of their of the issues works may need to be re scheduled or work to recommence on supervisors instructions

11. Emergencies First aid equipment is provided on each vehicle Emergency Reporting As per client procedure Emergency services Dial 999 Near Call 999 in the event of an emergency and state the incident location as [site address] Follow the instructions of the 999 call handler/emergency medical dispatcher until help arrives. Care must be taken to ensure that access for emergency vehicles is maintained throughout the site operations. Nearest Hospital is : ( Insert full address and map of nearest hospital with A&E facilities )

| Method statement prepared by: | Steven Cummings |
| --- | --- |
| Signed |  | Date |  |

Engineers Signature:

When on site to confirm you have read and understood the content of this method statement.

……………………………………………………………………………

……………………………………………………………………………

……………………………………………………………………………

……………………………………………………………………………

……………………………………………………………………………

……………………………………………………………………………

……………………………………………………………………………