Gas Monitors

- Clean by wiping with an anti bacterial cloth.

- Look for any damage.

- Check battery status.

Harness

- Check adjusters and attachment points for corrosion and ensure they adjust easily but hold their adjusted position.

- Check that there is no fraying cuts or tears of the webbing. If so do not use the harness, quarantine and send for repairs.

- A visual inspection in no way gives an indication of the webbing materials. It is important that the users report exposure to liquid or substances, if this happens then advice must be sought from the manufacturer.

Tripod and Winch

Winch

- Check that all the equipment functions according to manufacturer specifications.

- Position lock engages.

- Handle brake and release mechanisms.

- Eternal pawls and ratchets engage.

- Fall arrest operates.

- Steel ropes should be fully extended and a cloth placed around the rope and run up and down its entire length. If cloth snags then steel rope should be replaced.

Tripod

- Visual check for cracks.

- Excessive wear around boltholes and attachment points.

- Visually check bolts for tightness and all pins are in place.

- Limit chains must be complete together with other relevant accessories.