10 Minute Escape Set - Testing

The Bag

- Check it is not damaged in anyway.

- Check the webbing of handle, ensure it is intact.

- Check that the pull cord is fixed to the lid or connection clip is attached to the valve.

- Check that the Press Stud / Velcro will secure the lid.

Air Cylinder

- Must be grey with black and white top.

- Check test date (not more than 5 years)

- Check for signs of damage to cylinder or valve.

- Check gauge GREEN full (10 minutes air). RED - DO NOT USE.

Tube

- Check for any cuts or abrasions.

- Check reducer – condition of black ‘O’ ring in reducer.

- Check tube connection into hood.

Air Hood

- Examine the hood for wear or damage.

- Check condition of elasticated neckband.

- Check air supply hose connection is secure.