Civil Engineering Safety Ltd

Unit 1

Park Farm

Wood Lane

Ramsey

Cambridgeshire

PE26 2XA

Tel: 01480 431111

Fax: 01480 431113

Website: www.civilsafety.co.uk

Confined Space

Classifications

WATER UK Classification of Confined Spaces Entries

NC1- NC4

2008 New City and Guilds training titles

6150-01:	Level 2 Working in Low Risk

6150-02:	Level 2 Working in Medium Risk

6150-03:	Level 2 Working in High Risk

National Classification 4

Definition

NC4 / 6150-03

- Non standard entries involving complex operations

- which introduce additional risks

- and require specific controls and rescue arrangements

Examples; mechanical hazards, physical complexity of systems introduced hazards, enhanced specific intrinsic hazards.

National Classification 1
Definition

NC1 / 6150-01 Low risk shallow entry (not exceeding 1.5m)

- Adequate or natural ventilation

- Access is simple-unobstructed

- No Flood risk

Examples:

- Meter pits

- Valve Chambers

- Booster-pumping stations

- PRV Chambers

National Classification 2

Definition

NC2 / 6150-02

- Vertical direct unobstructed access

- Continuous attachment to a man riding hoist or similar mechanical rescue device.

National Classification 3

Definition

NC3  / 6150-03

When it is not possible to have persons permanently attached to a safety line.

Usually it will be a team entry which moves away from the entry point.

Working without an attached rescue line and includes working away from the point of entry.

Examples;  Man entry sewers, utility service, aqueducts and complex wet wells.